## Slide 1: Forecasting energy availability from renewable sources

## Slide 2: Introduction
In light of rising energy costs, the company seeks to introduce a service providing free energy to local clients near renewable sources during surplus energy periods. With a pilot project slated for May 2024, our immediate focus is on developing a predictive system to forecast surplus energy at least 24 hours in advance. This introduction outlines our goal to assess feasibility, minimize false positives, and pave the way for successful implementation, leveraging historic energy data at our disposal.

## Slide 3: Objective
Analyze historical energy records to identify patterns and trends related to excess renewable energy.
Develop a predictive model to forecast excess renewable energy conditions with a minimum lead time of 24 hours.
Validation and Testing: Validate the model on unseen data to ensure its generalizability and robustness. Conduct thorough testing to confirm that the model performs reliably across different scenarios and time periods.
Determine appropriate threshold points for excess energy through external studies and research.
Analyze if the model is ready for deployment in May 2024

## Slide 4: Methodology
Historical weather data of Brighton from 2010-2024
Data cleaning and Preprocessing to address missing values, outliers, and inconsistencies.
Split the dataset
  Train Set: 2010 – 2019
  Validation Set: 2020 - 2021
  Test Set: 2022 - 2024
Design and train two Recurrent Neural Network (RNN) models with Long Short-Term Memory (LSTM) layers:
  Model 1: Forecast solar energy production 24 hours in advance.
  Model 2: Forecast wind energy production 24 hours in advance.

## Slide 5: Assumptions and Research
Wind energy calculation
  Air density: 1.225kgm-3
  The windmill's dimensions, i.e., turbine radius, and swept area of the turbine are assumed to be 12m and 452.4 m2 respectively.
  The assumed number of windmills is 116 in Brighton
Solar energy calculation
  Solar Panel efficiency is assumed to be 20%
  Panel surface area: 20m2
  The assumed number of solar panels is 369 in Brighton

## Slide 6: Assumptions and Research
Energy Surplus Threshold
  No of households in Brighton: 121,401
  Average hourly energy usage per household: 0.38kWh
  Average hourly energy consumption all over Brighton households: 46.13 MWh
  Consumer behavior factor: 2
  Assumed Threshold: 95 mW
Model selection
  Extensive research and testing is done to find the best model for the defined problem – RNN with LSTM architecture
Electricity cost per 1 Megawatt: £50

## Slide 7: Results
Solar Energy data showing clear seasonal trends.

## Slide 8: Results
Wind Energy data does not show us a clear seasonal trend.

## Slide 9: Solar energy forecasting model performance on the validation set
  The average squared difference between the predicted values and the true values (Mean Squared Error) : 0.0077
  R-Squared: 0.912 indicates our model fits the data very well.

## Slide 10: Wind energy forecasting model performance on the validation set
  The average squared difference between the predicted values and the true values (Mean Squared Error): 20.665
  R-Squared: 0.822 indicates our model fits the data well but not as well as it fits for solar energy.

## Slide 11: Solar energy forecasting model performance on the test set
  The average squared difference between the predicted values and the true values (Mean Squared Error) : 0.01
  R-Squared: 0.886 indicates our model fits the data very well.

## Slide 12: Wind energy forecasting model performance on the test set
  The average squared difference between the predicted values and the true values (Mean Squared Error): 22.42
  R-Squared: 0.79 indicates our model is comparatively not performing well for wind energy.

## Slide 13: Total Energy Analysis
  Threshold: 95 mW
  False Positives: 2

## Slide 14: False Positives Analysis
Cost: £50 for 1mW
Datetime | Total Energy | Total Energy - Predicted | Difference | Cost in GBP
2022-02-18 16:00:00 | 60.18 | 106.30 | 46.12 | 2306.392
2022-11-01 03:00:00 | 68.25 | 108.64 | 40.39 | 2019.522
Total estimated cost to the company £4325.91

## Slide 15: Monthly Model Performance on Test Set

## Slide 16: Conclusions and Recommendations
Conclusions:
  Model predicted 2 false positives which will incur a £4325.91 loss for the company
  Model performance in May is 75%, indicating its effectiveness in capturing the variability in energy production during that month.
  We can conclude that the model is feasible and ready to be deployed in May 2024
Recommendations and future work:
  Look for better alternatives to predict wind energy.
  Continuously monitor and evaluate the model's performance post-deployment.
  Conduct a thorough cost-benefit analysis to evaluate the economic impact of deploying the model.

## Slide 17: References
https://www.rampionoffshore.com/#:~:text=The%20wind%20farm%20comprises%20116,coast%20in%20the%20English% 20Channel
https://www.e-education.psu.edu/emsc297/node/649#:~:text=Thus%2C%20the%20power%20available%20to,variable%20input%20is%20wind%20speed
https://www.brighton-hove.gov.uk/news/2023/hundreds-council-homes-switch-solar-power
https://www.saurenergy.com/solar-energy-blog/here-is-how-you-can-calculate-the-annual-solar-energy-output-of-a-photovoltaic-system
https://lginform.local.gov.uk/reports/lgastandard?mod-metric=3801&mod-area=E06000043&mod-group=AllUnitaryLaInCountry_England&mod-type=namedComparisonGroup
https://www.utilitybidder.co.uk/compare-business-energy/what-is-the-average-household-energy-usage/#:~:text=What%20is%20the%20average%20electricity,factors%20that%20affect%20this%20figure
https://www.brighton-hove.gov.uk/sites/default/files/2024-03/census-2021-briefing-city-profile_Muna%20Mohamed.pdf
https://businessenergycomparison.com/business-electricity/price-of-1-mwh-of-electricity-in-2023/#:~:text=Price%20Of%201%20MWh%20Electricity,focus%20on%20wholesale%20electricity%20prices
https://www.greenbuildingrenewables.co.uk/guide-to-solar-energy-as-electricity-prices-increase/

## Slide 18: Thank You🙂